## Slide 1
interface GigabitEthernet0/0
ipv6 address 2001:db8:1::1/64
no shutdown
interface GigabitEthernet0/1
ipv6 address 2001:db8:2::1/64
no shutdown
IPv6 Interface Configuration

## Slide 3
IPv6 Interface Configuration
interface GigabitEthernet0/0
ipv6 address 2001:db8:1::1/64
no shutdown
interface GigabitEthernet0/1
ipv6 address 2001:db8:2::1/64
no shutdown
ipv6 unicast-routing
Enable IPv6 Routing
Explanation: This configures IPv6 addresses on the router’s interfaces connected to different departments (Sales, HR, Support). The no shutdown command enables the interface. Each interface has a unique IPv6 subnet for proper routing and isolation.

## Slide 4
Enable IPv6 Routing
ipv6 unicast-routing
interface GigabitEthernet0/0
ipv6 ospf 1 area 0
interface GigabitEthernet0/1
ipv6 ospf 1 area 0
ipv6 router ospf 1
router-id 1.1.1.1
OSPFv3 Configuration
Explanation: Enables the router to forward IPv6 packets. Without this, the router won’t route IPv6 traffic between interfaces.

## Slide 5
OSPFv3 Configuration
interface GigabitEthernet0/0
ipv6 ospf 1 area 0
interface GigabitEthernet0/1
ipv6 ospf 1 area 0
ipv6 router ospf 1
router-id 1.1.1.1
hostname R1
ip domain-name project.local
crypto key generate rsa
1024
username admin secret cisco123
line vty 0 4
transport input ssh
login local
SSH Configuration
Explanation: Configures OSPFv3, the IPv6 version of OSPF, which dynamically shares routing info between routers. The router-id uniquely identifies each router in the OSPF domain.

## Slide 6
SSH Configuration
hostname R1
ip domain-name project.local
crypto key generate rsa
1024
username admin secret cisco123
line vty 0 4
transport input ssh
login local
ipv6 access-list BLOCK_SALES_TO_HR
deny ipv6 2001:db8:1::/64 2001:db8:2::/64
permit ipv6 any any
interface GigabitEthernet0/0
ipv6 traffic-filter BLOCK_SALES_TO_HR in
ACL - Block Sales to HR

## Slide 7
ACL - Block Sales to HR
ipv6 access-list BLOCK_SALES_TO_HR
deny ipv6 2001:db8:1::/64 2001:db8:2::/64
permit ipv6 any any
interface GigabitEthernet0/0
ipv6 traffic-filter BLOCK_SALES_TO_HR in
interface FastEthernet0/1
switchport mode access
switchport port-security
switchport port-security maximum 1
switchport port-security mac-address sticky
switchport port-security violation restrict
Port Security

## Slide 8
Port Security
interface FastEthernet0/1
switchport mode access
switchport port-security
switchport port-security maximum 1
switchport port-security mac-address sticky
switchport port-security violation restrict
ip dhcp snooping
ip dhcp snooping vlan 10,20,30
interface GigabitEthernet0/1
ip dhcp snooping trust
interface range GigabitEthernet0/2 - 24
ip dhcp snooping limit rate 10
DHCP Snooping

## Slide 9
DHCP Snooping
ip dhcp snooping
ip dhcp snooping vlan 10,20,30
interface GigabitEthernet0/1
ip dhcp snooping trust
interface range GigabitEthernet0/2 - 24
ip dhcp snooping limit rate 10
vlan 10
name HR
vlan 20
name Sales
vlan 30
name Support
interface vlan 10
ip address 192.168.10.1 255.255.255.0
no shutdown
ip routing
VLANs & Inter-VLAN Routing

## Slide 10
VLANs & Inter-VLAN Routing
vlan 10
name HR
vlan 20
name Sales
vlan 30
name Support
interface vlan 10
ip address 192.168.10.1 255.255.255.0
no shutdown
ip routing
interface GigabitEthernet0/1
switchport trunk encapsulation dot1q
switchport mode trunk
Trunk Port Configuration

## Slide 11
Trunk Port Configuration
interface GigabitEthernet0/1
switchport trunk encapsulation dot1q
switchport mode trunk
interface Tunnel0
ip address 10.10.10.1 255.255.255.0
tunnel source Serial0/0/0
tunnel destination [REMOTE_ROUTER_PUBLIC_IP]
VPN Tunnel (GRE)

## Slide 12
VPN Tunnel (GRE)
interface Tunnel0
ip address 10.10.10.1 255.255.255.0
tunnel source Serial0/0/0
tunnel destination [REMOTE_ROUTER_PUBLIC_IP]
ip arp inspection vlan 10,20,30
interface GigabitEthernet0/1
ip arp inspection trust
interface range GigabitEthernet0/2 - 24
ip arp inspection untrust
ARP Inspection

## Slide 13
ARP Inspection
ip arp inspection vlan 10,20,30
interface GigabitEthernet0/1
ip arp inspection trust
interface range GigabitEthernet0/2 - 24
ip arp inspection untrust
interface range FastEthernet0/10 - 24
shutdown
Disable Unused Ports

## Slide 14
Disable Unused Ports
interface range FastEthernet0/10 - 24
shutdown